## Slide 1
Lecture 17 - Fusion, Layout Propagation
1/35
AI/NPU Compiler를 위한 MLIR
Transformer MLP fusion 후보 분석
산출물: fusion/layout/cost contract + pseudo IR

## Slide 2
오늘의 위치
2/35
14강 Vector/Tensorization: native tile로 mapping
15강 Transform Dialect: schedule IR
16강 Quantization: numeric contract
17강: fusion/layout decision으로 NPU performance를 결정

## Slide 3
Learning Objectives
3/35
Fusion을 legality + cost + layout contract로 정의
Transformer MLP에서 fusion 후보를 체계적으로 분류
Layout propagation과 materialization boundary 설계
SRAM/ACCUM footprint와 traffic saving 계산
FileCheck 기반 regression test 작성

## Slide 4
왜 Fusion인가?
4/35
Physical AI edge NPU는 DRAM bandwidth가 성능 병목인 경우가 많음
Intermediate tensor write/read 제거가 latency와 power를 줄임
Epilogue를 accumulator/SRAM 내부에서 처리하면 command 수와 DMA가 감소
단, fusion이 live range와 SRAM pressure를 증가시킬 수 있음
Rule: fusion must reduce traffic without violating SRAM, layout, or numeric contracts.

## Slide 5
Fusion의 세 수준
5/35
Op fusion: IR에서 semantic op를 결합
Kernel fusion: 하나의 NPU kernel로 lowering
Command fusion: command buffer에서 DMA/compute/barrier를 결합
각 수준마다 verifier와 test가 달라야 함

## Slide 6
Fusion Pipeline Overview
6/35

## Slide 7
Transformer MLP 구조
7/35
Classic: X -> GEMM1 -> Bias -> GELU -> GEMM2 -> Bias
Gated: gate/up projection -> SiLU -> Mul -> output projection
MLP intermediate는 H보다 4x 이상 커서 traffic 영향이 큼

## Slide 8
MLP Fusion Candidates
8/35

## Slide 9
Legality != Profitability
9/35
Legal: shape/dtype/layout/quant 조건을 만족
Profitable: saved traffic and cycles > extra live range/repack cost
NPU compiler는 두 조건을 분리해 debug해야 함
Keep legality and profitability as separate debug-visible decisions.

## Slide 10
Fusion Legality Fields
10/35
rank/static shape/dynamic dims
dtype and accumulator type
broadcast semantics
per-channel quant axis
layout compatibility
single-use or profitable multi-use

## Slide 11
Use-Def 기반 후보 탐지
11/35
Root op를 activation 또는 consumer matmul로 잡음
Producer chain을 거슬러 matmul/bias/elementwise 패턴 확인
multiple consumer는 cost model로만 허용
IR mutation 전에는 match-only로 실패 조건 수집

## Slide 12
Layout Propagation 개념
12/35
Logical shape와 physical layout을 분리
Elementwise/view-like op는 layout-preserving인 경우가 많음
Consumer preferred layout을 producer로 역전파 가능
불가피한 boundary에서만 explicit materialization 삽입

## Slide 13
대표 Layout
13/35

## Slide 14
Layout Propagation Rules
14/35
Propagate through elementwise, relu/gelu/silu approximation, scalar mul
Propagate through reshape if view-like and axis mapping known
Stop at unsupported reduction/gather/scatter/fallback
Insert npu_graph.layout_materialize with reason attr

## Slide 15
Quantization Axis 문제
15/35
Per-channel scale axis가 layout 변경 후에도 정확해야 함
N dimension blocking은 channel axis를 유지하는지 검증 필요
INT8/INT4 pack layout은 scale layout도 함께 정의해야 함
Mismatch는 silent accuracy bug가 될 수 있음
Quant axis mapping is part of layout propagation, not an afterthought.

## Slide 16
Cost Model: Traffic
16/35

## Slide 17
Cost Model: SRAM/ACCUM
17/35
Input/weight/output tile + accumulator + epilogue temp + double buffer
SwiGLU는 gate/up branch live range가 길어짐
ACCUM tile precision이 SRAM보다 더 제한적일 수 있음
Spill 발생 시 fusion benefit이 크게 감소

## Slide 18
Cost Model: Cycles
18/35
compute cycles = MAC / effective TOPS
DMA cycles = bytes / effective bandwidth
bank conflict and tensor core occupancy 포함
critical path는 max(compute, DMA) + barrier overhead

## Slide 19
Classic MLP Case Study
19/35
GEMM1 output: [tokens, 4H]로 큼
Bias+GELU는 ideal epilogue fusion 후보
GEMM2는 GELU output layout을 input layout으로 요구
Blocked activation을 GEMM2까지 유지할지 cost model로 결정

## Slide 20
SwiGLU Case Study
20/35
Gate and up projections produce two large intermediates
SiLU(gate) * up는 tile-local fusion 후보
두 branch 동시 live range가 SRAM을 압박
branch streaming 또는 split materialization 정책 필요

## Slide 21
Weight Prepack
21/35
Static weight는 compile/deploy time prepack 가능
Dynamic weight는 runtime cache와 invalidation 정책 필요
Prepack layout은 tensorization map과 DMA descriptor에 반영
Quant scale/zero-point도 packed axis에 맞춰 저장
Weight prepack changes runtime ABI and model packaging.

## Slide 22
Pass Design
22/35

## Slide 23
IR Contract: fused op
23/35
epilogue attr: bias_gelu_tanh, bias_relu, requant_clamp
layout attrs: lhs/rhs/out
accumulator attr: fp32/int32
fusion_id/debug metadata
materialization reason attrs

## Slide 24
Transform Dialect와 연결
24/35
Transform IR로 tile/fuse/vectorize 순서를 명시
Fusion decision은 transform schedule parameter가 될 수 있음
Schedule YAML과 transform IR을 연결하면 autotuning에 유리
Payload IR과 schedule IR을 분리해 review 가능

## Slide 25
Testing Strategy
25/35
Positive: fused op 생성과 attr 확인
Negative: unsupported shape/layout/quant에서는 no fusion
CHECK-NOT: unfused bias/activation 제거
materialization op count 제한
numeric golden test로 approximation 검증
Tests should catch both over-fusion and missed materialization.

## Slide 26
Debug Recipe
26/35
1. print candidate groups
2. print legality failure reason
3. print layout propagation trace
4. print cost model table
5. compare profiler counters with expected bytes

## Slide 27
Common Failure #1
27/35
Pattern은 맞지만 broadcast axis가 다름
Bias shape [M,N] vs [N] 차이
잘못 fuse하면 semantic bug
Verifier에서 broadcast contract를 검사

## Slide 28
Common Failure #2
28/35
Layout propagation 후 per-channel quant axis mismatch
Scale tensor layout 업데이트 누락
INT8/INT4 requant에서 accuracy regression
Axis mapping metadata를 mandatory로 둠

## Slide 29
Common Failure #3
29/35
Fusion으로 live range가 증가해 SRAM spill 발생
Traffic saving보다 spill/repack이 더 큼
Cost model 없이 greedy fusion 금지
Negative performance test 필요

## Slide 30
실습 A
30/35
01_transformer_mlp_before.mlir을 읽고 fusion candidate를 표시
root op, producer chain, consumer chain 작성
multiple-use 여부 표시

## Slide 31
실습 B
31/35
Layout propagation graph 작성
blocked layout을 어디까지 유지할지 결정
materialization point와 reason attr 정의

## Slide 32
실습 C
32/35
07_memory_traffic_calculator.py 실행
unfused vs fused writes 비교
SRAM budget을 바꿔 fallback decision 작성

## Slide 33
실습 D
33/35
npu_graph.matmul_epilogue pseudo IR 작성
epilogue/layout/accumulator/fusion_id attr 포함
FileCheck positive/negative test 작성

## Slide 34
Takeaways
34/35
Fusion is a contract, not just a rewrite
Layout propagation removes hidden copy/repack overhead
Transformer MLP is the best practice case for NPU fusion analysis
Cost model must include bytes, cycles, SRAM, layout, quantization
Final output: fused pseudo IR + layout propagation graph + cost table.

## Slide 35
References
35/35
MLIR Linalg Dialect
MLIR Transform Dialect
MLIR Data Layout Modeling
MLIR MemRef Dialect
MLIR Transform Tutorial Chapter 0